## Slide 1: Computer Architecture ----A Quantitative Approach
陈文智
浙江大学计算机学院
chenwz@zju.edu.cn

## Slide 2: Tomasulo Drawbacks
Complexity
  delays of 360/91, MIPS 10000, Alpha 21264, IBM PPC 620 in CA:AQA 2/e, but not in silicon!
Many associative stores (CDB) at high speed, Performance limited by Common Data Bus
Non-precise interrupts!
  We will address this later
Partially overlapped basic blocks
  integer units get ahead, beyond FP operation
  the successor basic block can not start execution until the branch is resolved, in spite of that it can be issued.

## Slide 3: Hardware-based Speculation
Speculating on the outcome of branches and executing the program as if the predictions were correct.
  Need to handle the situation where the speculation is incorrect.
Key ideas:
  Dynamic branch prediction to choose which instruction to execute
  Speculation to allow the execution of instructions before the control dependences are resolved.
  Dynamic scheduling to deal with the scheduling of different combinations of basic blocks.
Data flow execution:
  Operations execute as soon as their operands are available.

## Slide 4: Speculative execution with Tomasulo's algorithm
Separate the process of completing execution and the bypassing of results among instructions from instruction commit (reg file or memory update).
Allows other (speculative) instructions to execute, but no results are committed until we know the instruction is no longer speculative.
Allow instructions to execute out of order but force them to commit in order, which helps with handling exceptions properly.

## Slide 5: Extend Tomasulo to handle speculation

## Slide 6: Extend Tomasulo to handle speculation
FP adders
Add1
Add2
Add3
FP multipliers
Mult1
Mult2
From Mem
FP Registers
Reservation
Stations
Common Data Bus (CDB)
To Mem
FP Op
Queue
Load Buffers
Store
Buffers
Load1
Load2
Load3
Load4
Load5
Load6
From Intruction unit

## Slide 7: Difference from Tomasulo Algorithm
Reorder Buffer is added
Eliminate store buffer (Mem write is ordered in Reorder buffer)
Register renaming is done via reorder buffer instead of reservation station
Reservation only for storing opcodes and operands during the instruction flying between issue and execution.
ROB hold the instruction results and supply operands in the interval between completion of instruction execution and instruction commit.

## Slide 8: Entry of ROB
Instruction type
Destination field
Value field
Ready field
Exception vector

## Slide 9: 4 Steps of Speculative Tomasulo Algorithm
Issue—get instruction from FP Op Queue
  If reservation station and reorder buffer slot free, issue instr & send operands & reorder buffer no. for destination (this stage sometimes called “dispatch”) , update control entries “in use”.
Execution—operate on operands (EX)
  When both operands ready then execute; if not ready, watch CDB for result; when both in reservation station, execute; checks RAW
Write result—finish execution (WB)
  Write on Common Data Bus to all awaiting FUs & reorder buffer; mark the reservation station available.
Commit—update register with reorder result
  When instruction at head of reorder buffer & result present, update register with result (or store to memory) and remove instr from reorder buffer. Mispredicted branch flushes reorder buffer (sometimes called “graduation”)

## Slide 10: What to do when commit ?
When an instruction reaches the head of ROB and its result is present in the buffer, then
For non-Branch instruction
  Update the register with the result
  Remove the instruction from ROB
  When it’s a STORE, update the memory instead of Reg.
For a mispredicted branch
  ROB is flushed and execution is restarted at the correct successor of the branch
For a right-predicted branch
  End of branch instruction.

## Slide 11: 2 clock cycles for pipelined memory access
LD F6,34(R2)
LD F2,45(R3)
MULD F0,F2,F4
SUBD F8,F2,F6
DIVD F10,F0,F6
ADDD F6,F8,F2
LD F6,34(R2)
Dest
Oldest
Newest
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F6
LD F6,34(R2)
N
Done?
Dest
from
Memory
1 34+R2
Dest
Reorder Buffer
Registers
Busy, ROB No. Value

## Slide 12: Tomasulo With Reorder buffer:
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F2
F6
LD F2,45(R3)
LD F6,34(R2)
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
1 34+R2
2 45+R3
LD F6,34(R2)
LD F2,45(R3)
MULD F0,F2,F4
SUBD F8,F2,F6
DIVD F10,F0,F6
ADDD F6,F8,F2

## Slide 13: Tomasulo With Reorder buffer:
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
3 MULD ROB2,R(F4)
F0
F2
F6
MULD F0,F2,F4
LD F2,45(R3)
LD F6,34(R2)
N
N
N
1 34+R2
2 45+R3
LD F6,34(R2)
LD F2,45(R3)
MULD F0,F2,F4
SUBD F8,F2,F6
DIVD F10,F0,F6
ADDD F6,F8,F2

## Slide 14: Tomasulo With Reorder buffer:
4 SUBD ROB2,ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
3 MULD ROB2,R(F4)
1 34+R2
2 45+R3
N
N
F8
SUBD F8,F2,F6
N
F0
F2
F6
MULD F0,F2,F4
LD F2,45(R3)
LD F6,34(R2)
N
N
N
LD F6,34(R2)
LD F2,45(R3)
MULD F0,F2,F4
SUBD F8,F2,F6
DIVD F10,F0,F6
ADDD F6,F8,F2
Note: The first LD will finish memeory access next cycle

## Slide 15: Tomasulo With Reorder buffer:
4 SUBD ROB2,M[34+R2]
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
3 MULD ROB2,R(F4)
2 45+R3
N
N
F8
SUBD F8,F2,F6
N
F0
F2
F6
MULD F0,F2,F4
LD F2,45(R3)
LD F6,34(R2)
N
N
Y
DIVD F10,F0,F6
F10
5 DIVD ROB3,M[34+R2]
M[34+R2]
LD F6,34(R2)
LD F2,45(R3)
MULD F0,F2,F4
SUBD F8,F2,F6
DIVD F10,F0,F6
ADDD F6,F8,F2
Note: The 2nd LD will finish memeory access next cycle
1 34+R2

## Slide 16: Tomasulo With Reorder buffer:
4 SUBD M[45+R3],M[34+R2]
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
3 MULD M[45+R3],R(F4)
N
N
F8
SUBD F8,F2,F6
N
F0
F2
F6
MULD F0,F2,F4
LD F2,45(R3)
LD F6,34(R2)
N
Y
Y
DIVD F10,F0,F6
F10
5 DIVD ROB3,M[34+R2]
M[34+R2]
ADDD F6,F8,F2
F6
6 ADDD ROB4, M[45+R3]
M[45+R3]
LD F6,34(R2)
LD F2,45(R3)
MULD F0,F2,F4
SUBD F8,F2,F6
DIVD F10,F0,F6
ADDD F6,F8,F2
1 34+R2
2 45+R3

## Slide 17: Tomasulo With Reorder buffer:
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
3 MULD M[45+R3],R(F4)
N
N
F8
SUBD F8,F2,F6
Y
F0
F2
F6
MULD F0,F2,F4
LD F2,45(R3)
LD F6,34(R2)
N
Y
Y
DIVD F10,F0,F6
F10
5 DIVD ROB3,M[34+R2]
M[34+R2]
ADDD F6,F8,F2
F6
6 ADDD V[1], M[45+R3]
M[45+R3]
V[1]
LD F6,34(R2)
LD F2,45(R3)
MULD F0,F2,F4
SUBD F8,F2,F6
DIVD F10,F0,F6
ADDD F6,F8,F2

## Slide 18: Speculation performance
Overlapped basic block
Is there any new problems ?
  Pay attention to the memory accessing

## Slide 19: Tomasulo With Reorder buffer:
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F0
LD F0,10(R2)
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers

## Slide 20: Tomasulo With Reorder buffer:
2 ADDD R(F4),ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F10
F0
ADDD F10,F4,F0
LD F0,10(R2)
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers

## Slide 21: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers

## Slide 22: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
6 ADDD ROB5, R(F6)
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F0
ADDD F0,F4,F6
N
F4
LD F4,0(R3)
N
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
5 0+R3

## Slide 23: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
6 ADDD ROB5, R(F6)
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
ROB5
ST 0(R3),F4
ADDD F0,F4,F6
N
N
F4
LD F4,0(R3)
N
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
1 10+R2
6 0+R3

## Slide 24: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
M[10]
ST 0(R3),F4
ADDD F0,F4,F6
Y
N
F4
M[10]
LD F4,0(R3)
Y
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
2 ADDD R(F4),ROB1
6 ADDD M[10],R(F6)

## Slide 25: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
M[10]
<val2>
ST 0(R3),F4
ADDD F0,F4,F6
Y
Ex
F4
M[10]
LD F4,0(R3)
Y
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers

## Slide 26: Tomasulo With Reorder buffer:
--
F0
M[10]
<val2>
ST 0(R3),F4
ADDD F0,F4,F6
Y
Ex
F4
M[10]
LD F4,0(R3)
Y
--
BNE F2,<…>
N
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
What about memory
hazards???

## Slide 27: new problem--memory disambiguation
Question: Given a load that follows a store in program order, are the two related?
  (Alternatively: is there a RAW hazard between the store and the load)? Eg: ST 0(R2), R5 LD R4, 0(R3)
Can we go ahead and start the load early?
  Store address could be delayed for a long time by some calculation that leads to R2 (divide?).
  We might want to issue/begin execution of both operations in same cycle.

## Slide 28: Tomasulo With Reorder buffer:
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
-
ST R5,0(R2)
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers

## Slide 29: Tomasulo With Reorder buffer:
2 ADDD R(F4),R（F0)
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F10
-
ADDD F10,F4,F0
ST R5,0(R2)
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers

## Slide 30: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4),R(F0)
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F2
F10
-
DIVD F2,F10,F6
ADDD F10,F4,F0
ST R5,0(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers

## Slide 31: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4), ROB?
6 ADDD ROB5, R(F6)
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F0
ADDD F0,F4,F6
N
F4
LD F4,0(R3)
N
--
BNE F2,<…>
N
F2
F10
-
DIVD F2,F10,F6
ADDD F10,F4,F0
ST R5,0(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
4 0+R3
Dest
Reorder Buffer
Registers

## Slide 32: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4),R(F0)
6 ADDD ROB5, R(F6)
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
ROB5
ST 0(R3),F4
ADDD F0,F4,F6
N
N
F4
LD F4,0(R3)
N
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
ST R5,0(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
4 0+R3

## Slide 33: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
M[10]
ST 0(R3),F4
ADDD F0,F4,F6
Y
N
F4
M[10]
LD F4,0(R3)
Y
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
ST R5,0(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
4 0+R3
Dest
Reorder Buffer
Registers
2 ADDD R(F4), ROB?
6 ADDD M[10],R(F6)

## Slide 34: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4), ROB?
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
M[10]
<val2>
ST 0(R3),F4
ADDD F0,F4,F6
Y
Ex
F4
M[10]
LD F4,0(R3)
Y
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
ST R5,0(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
4 0+R3
Dest
Reorder Buffer
Registers

## Slide 35: Tomasulo With Reorder buffer:
--
F0
M[10]
<val2>
ST 0(R3),F4
ADDD F0,F4,F6
Y
Ex
F4
M[10]
LD F4,0(R3)
Y
--
BNE F2,<…>
N
3 DIVD ROB2,R(F6)
2 ADDD R(F4), ROB?
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
ST R5,0(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
4 0+R3
Dest
Reorder Buffer
Registers
What if 0(R3)=0(R2)

## Slide 36: Sorting out RAW Hazards in memory
Question: Given a load that follows a store in program order, are the two related?
  (Alternatively: is there a RAW hazard between the store and the load)? Eg: ST 0(R2), R5 LD R6, 0(R3)
Can we go ahead and start the load early?
  Store address could be delayed for a long time by some calculation that leads to R2 (divide?).
  We might want to issue/begin execution of both operations in same cycle.
  Today: Answer is that we are not allowed to start load until we know that address 0(R2) ≠ 0(R3)

## Slide 37: Hardware Support for Memory Disambiguation
Need buffer to keep track of all outstanding stores to memory, in program order.
  Keep track of address (when becomes available) and value (when becomes available)
  FIFO ordering: will retire stores from this buffer in program order
When issuing a load, record current head of store queue (know which stores are ahead of you).

## Slide 38: Hardware Support for Memory Disambiguation(2)
When have address for load, check store queue:
  If any store prior to load is waiting for its address, stall load.
  If load address matches earlier store address (associative lookup), then we have a memory-induced RAW hazard:
    store value available → return value
    store value not available → return ROB number of source
  Otherwise, send out request to memory
Actual stores commit in order, so no worry about WAR/WAW hazards through memory.

## Slide 39: Memory Disambiguation:
F4
LD F4, 10(R3)
N
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
--
<val 1>
ST 10(R3), F5
LD F0,32(R2)
ST 0(R3), F4
N
N
Y
Done?
Dest
Dest
Oldest
Newest
from
Memory
2 32+R2
4 ROB3
Dest
Reorder Buffer
Registers

## Slide 40: HW support for precise interrupts
Need HW buffer for results of uncommitted instructions: reorder buffer
  3 fields: instr, destination, value
  Use reorder buffer number instead of reservation station when execution completes
  Supplies operands between execution complete & commit
  (Reorder buffer can be operand source => more registers like RS)
  Once instruction commits, result is put into register
  As a result, easy to undo speculated instructions on mispredicted branches or exceptions
Reorder
Buffer
FP
Op
Queue
FP Adder
FP Adder
Res Stations
Res Stations
FP Regs

## Slide 41
 | 记分牌 | Tomasulo | 带投机的Tomasulo
主要 思想 | 动态调度、按序发射、乱序 执行、乱序完成、集中控制。 | 动态调度、按序发射、乱序 执行、乱序完成分散控制。 增加RS（保留站）,CDB。 | 转移预测, 动态调度、投机执行、 按序完成。在RS基础上再增加ROB(reorder buffer)。
解决 何种 竞争 | RAW数据竞争。 WAW,WAR时stall | 解决数据竞争,避免WW,WAR 竞争;允许硬件支持的循环展 开，不局限于程序基本块。 | 解决数据竞争,避免WW,WAR 竞争;从数据竞争扩充到控制竞争。通过 预测减少控制竞争stall。
指 令 节 拍 | ISSUE：停顿于结构竞争和WAW竞争。 RO：等待两个操作数就绪,动态解决RAW。 EX：和普通流水线一样。 WB：停顿于WAR竞争。 | ISSUE：仅停顿于结构竞争（RS部件）。 EX：利用保留站（RS）进行换名，解决了WAW和WAR问题（即名字相关）。 WB：回写。 | ISSUE：仅停顿于结构竞争（RS部件和ROB部件）。 EX：等待操作数就绪，执行。 WB：结果写到ROB，其它指令可以引用该临时结果，但不更新寄存器。 COMMIT：保证按序完成，保证精确中断。
关键 部件 | 记分牌、集中控制、指令状 态、功能部件状态、寄存器 结果状态。 | CDB(通用数据总线)：执行结果通过CDB传递，及时。 RS(保留站)：换名功能以及暂存临时数据。 | ROB(REORDER BUFFER)重构序缓冲器： 对移到顶部的指令进行判断。。。ROB 负责寄存器重命名、暂存执行后和交付 前的结果、
其它 | 从静态调度到动态调度的过 渡算法。 | 一旦指令将临时结果放在保留站，则其它后续的指令都能立即在寄存器组中看见这个结果。 | 某指令将临时结果放在ROB后，其它指 令并不能从寄存器组中看到这个结果 （也就是说，寄存器组的值并没有更 新），而是等待该指令提交（commit） 后，寄存器组才更新。

## Slide 42
THANK YOU
THANK YOU