## Slide 1: Computer Architecture ----A Quantitative Approach
陈文智
浙江大学计算机学院
chenwz@zju.edu.cn

## Slide 2: Review – explore ILP via Hardware approaches
Basic 5-stage pipeline
Extended to pipeline supporting FP operations
Scoreboard
Tomasulo Algorithm
Branch predictor
Hardware-based Speculation
Explicit register renaming

## Slide 3: Review:
Forwarding
  Reduce potential data hazard stalls.
Delayed branch
  Reduce control stalls with simple branch scheduling
Dynamic scheduling
  Scoreboard:
    reduce data stalls from true data dependence
  Tomasulo:
    Eliminate data stalls from WAR & WAW data dependences via renaming
    Reduce data hazard stalls via out-of-order execution
Branch predictor
  Reduce control stalls
Hardware-based speculation
achieve an ideal CPI = 1 !

## Slide 4: Getting CPI < 1: Multiple Issue Processors
Vector Processing: Explicit coding of independent loops as operations on large vectors of numbers
  Multimedia instructions being added to many processors
Superscalar: varying number of instructions/cycle (1 to 8), scheduled by compiler or by HW (Tomasulo)
  IBM PowerPC, Sun UltraSparc, DEC Alpha, Pentium III/4
(Very) Long Instruction Words (V)LIW: fixed number of instructions (4-16) scheduled by the compiler; put ops into wide templates (TBD)
  Intel Architecture-64 (IA-64) 64-bit address
    Renamed: “Explicitly Parallel Instruction Computer (EPIC)”
Anticipated success of multiple instructions lead to Instructions Per Clock cycle (IPC) vs. CPI

## Slide 5: Explore ILP via Multiple-issue
Goal:
  Allow multiple instructions to issue in a clock cycle. Getting CPI < 1:
Approach
  Static Superscalar
  Dynamic Superscalar
  Speculative Superscalar
  VLIW/LIW
  EPIC( IA-64)

## Slide 6: Comparison
 | Issue Structure | Hazard Detection | Scheduling | Characteristic | examples
Superscalar (static) | Dynamic | Hardware | Static | In-order execution | Sun UltraSPARCII
Superscalar (dynamic) | Dynamic | Hardware | Dynamic | Some out-or-order exec. | IBM Power2
Superscalar (speculative) | Dynamic | Hardware | Dynamic With speculation | Out-of-order exec. With speculation | Pentium III/4 MIPS R10K, Alpha 21264
VLIW/ LIW | Static | Software | Static | No hazards in issue packets | Trimedia, i860
EPIC | Mostly static | Mostly software | Mostly static | Explicit dependences marked by compiler | Itanium

## Slide 7: Superscalar
the processor tries to issue more than one instruction (varying number 1-8) per cycle so as to keep all of the functional units busy.
  Statically scheduled
    using compiler techniques
    In-order execution
  Dynamically scheduled
    using techniques based on Tomasulo’s algorithm
    Out-of-order execution

## Slide 8: Statically Scheduled Superscalar
Instruction issue in order
All pipeline hazards are checked for at issue time. May issue 0~8 instructions per Clockcycle.
Issue packet: the instruction group received from the fetch unit that potentially issue in one clock cycle.
Issue stage is split and pipelined:
Decide how many instructions from the packet can issue simultaneously (within packet )
Detect hazards among the selected instructions and those that have already been issued.(between packet)

## Slide 9: An example of dual-issue pipeline

## Slide 10: Ex. Superscalar MIPS
2 instructions, 1 FP & 1 anything
  Fetch 64-bits/clock cycle; Int on left, FP on right
  Can only issue 2nd instruction if 1st instruction issues
  More ports for FP registers to do FP load & FP op in a pair
1 cycle load delay expands to 3 instructions in Superscalar
  instruction in right half can’t use it, nor instructions in next slot
Branch delay for a taken branch becomes either two or three instructions

## Slide 11: Superscalar MIPS pipeline in operation

## Slide 12: Multiple Issues
issue packet: group of instructions from fetch unit that could potentially issue in 1 clock
  If instruction causes structural hazard or a data hazard either due to earlier instruction in execution or to earlier instruction in issue packet, then instruction does not issue
  0 to N instruction issues per clock cycle, for N-issue
Performing issue checks in 1 cycle could limit clock cycle time: O(n2-n) comparisons
  => issue stage usually split and pipelined
  1st stage decides how many instructions from within this packet can issue, 2nd stage examines hazards among selected instructions and those already been issued
  => higher branch penalties => prediction accuracy important

## Slide 13: Multiple Issue Challenges
While Integer/FP split is simple for the HW, get CPI of 0.5 only for programs with:
  Exactly 50% FP operations AND No hazards
If more instructions issue at same time, greater difficulty of decode and issue:
  Even 2-scalar => examine 2 opcodes, 6 register specifiers, & decide if 1 or 2 instructions can issue; (N-issue ~O(N2-N) comparisons)
  Register file: need 2*N reads and 1*N writes/cycle

## Slide 14: Multiple Issue Challenges(cont.)
Rename logic: must be able to rename same register multiple times in one cycle! For instance, consider 4-way issue:
add r1, r2, r3 add p11, p4, p7 sub r4, r1, r2 → sub p22, p11, p4 lw r1, 4(r4) lw p23, 4(p22) add r5, r1, r2 add p12, p23, p4
Imagine doing this transformation in a single cycle!
Result buses: Need to complete multiple instructions/cycle
  So, need multiple buses with associated matching logic at every reservation station.
  Or, need multiple forwarding paths

## Slide 15: Dynamically Scheduled Superscalar
Potentially overcome the issue restrictions.
Two different approaches to issue multiple instructions per clock:
  Pipeline: Run this step in half a clock cycle, so that two instructions can be processed in one clock cycle.
  Widen issue logic: Build the logic necessary to handle two instructions at once, including any possible dependences between the instructions.
  Both: Modern superscalar processors often include both pipeline and widen the issue logic.

## Slide 16: Example
Assumptions:
  1 FP and 1 integer operation per CC. even if they are dependent.
  One integer function unit for ALU and address calculations
  Separate function unit for evaluating branch condition
  Single issue for branches, but perfect prediction.
  No speculation: all instr. following a branch are delay until branch resolved.
Loop: L.D F0, 0(R1)
ADD.D F4, F0, F2
S.D F4, 0(R1)
DADDIU R1, R1, #-8
BNE R1,R2, Loop
Function Latency:
1 cycle for integer ALU
2 cycles for load
3 cycles for FP add.

## Slide 17: Operation on a dual-issue version of Tomasulo
Structure hazard
No speculation
Structure hazard
Structure hazard
Integer function unit bottleneck
One memory unit, one interger pipeline, one FP adder

## Slide 18: Separate FU for ALU op and Address Calculation
A second CDB is needed !

## Slide 19: Multiple Issue with Speculation
A speculative processor can be extended to multiple issue.
Need to handle multiple instruction commits per clock cycle.
Example:
Loop: LD R2, 0(R1)
ADDI R2, R2, #1
SD R2, 0(R1)
ADDI R1, R1, #4
BNE R2, R3, Loop

## Slide 20: Assumptions
Separate integer function units for
  Effective address calculation
  ALU operations
  Branch condition evaluation

## Slide 21: Dual-issue without speculation

## Slide 22: Dual-issue with speculation

## Slide 23: Explore ILP via Software approaches
Basic Compiler Technique for Exposing ILP
  Loop unrolling
Static Branch Prediction
Static multiple Issue: VLIW
Advanced Compiler Support for Exposing and Exploiting ILP
  Software pipelining
  Global Code scheduling
Hardware Support for Exposing More Parallelism at compile time
  Conditional or Predicated instructions
  Compiler speculation with hardware support

## Slide 24: Review: Static Branch Prediction
Simplest: Predict taken
  average misprediction rate = untaken branch frequency, which for the SPEC programs is 34%.
  Unfortunately, the misprediction rate ranges from not very accurate (59%) to highly accurate (9%)
Predict on the basis of branch direction?
  choosing backward-going branches to be taken (loop)
  forward-going branches to be not taken (if)
  SPEC programs, however, most forward-going branches are taken => predict taken is better
Predict branches on the basis of profile information collected from earlier runs
  Misprediction varies from 5% to 22%

## Slide 25: Example:
For ( i=1000; i>0; i=i-1 )
x[i] = x[i] + s;

## Slide 26: First: Translate into MIPS code
Loop: LD F0,0(R1) ;F0=vector element
ADDD F4,F0,F2 ;add scalar from F2
SD 0(R1),F4 ;store result
SUBI R1,R1,8 ;decrement pointer 8B (DW)
BNEZ R1,R2,Loop ;branch if R1 != R2
NOP ;delayed branch slot
Instruction Instruction Latency producing result using result in cycles
FP ALU op Another FP ALU op 3
FP ALU op Store double 2
Load double FP ALU op 1
Load double Store double 0
Integer op Integer op 0

## Slide 27: Where are the Hazards?
1 Loop: L.D F0,0(R1)
2 stall
3 ADD.D F4,F0,F2
4 stall
5 stall
6 S.D 0(R1),F4
7 DSUBUI R1,R1,8
8 stall
9 BNEZ R1,R2,Loop
10 stall
Loop: LD F0, 0(R1)
ADDD F4, F0, F2
SD 0(R1), F4
SUBI R1, R1, #8
BNEZ R1,R2 Loop
F D X M W
F D s A1 A2 A3 A4 W
F s D s s X M W
F s s D X M W
F s D X M W
10 CC F F

## Slide 28: Reducing stalls from scheduling in Basic and delayed branch
Loop: LD F0, 0(R1)
SUBI R1, R1,#8
ADDD F4, F0, F2
BNEZ R1,R2 Loop
SD +8(R1), F4
Loop: LD F0, 0(R1)
ADDD F4, F0, F2
SD 0(R1), F4
SUBI R1, R1, #8
BNEZ R1,R2, Loop
F D X M W
F D s A1 A2 A3 A4 W
F s D s s X M W
F s s D X M W
F s D X M W
10 CC F F
F D X M W
F D X M W
F DA1A2A3A4W
F D X M W
F D s X M W
F s D X M W
6 CC

## Slide 29: Unroll Loop Four Times (straight forward)
Rewrite loop to minimize stalls?
1 Loop: LD F0,0(R1)
2 ADDD F4,F0,F2
3 SD 0(R1),F4 ;drop SUBI & BNEZ
4 LD F6,-8(R1)
5 ADDD F8,F6,F2
6 SD -8(R1),F8 ;drop SUBI & BNEZ
7 LD F10,-16(R1)
8 ADDD F12,F10,F2
9 SD -16(R1),F12 ;drop SUBI & BNEZ
10 LD F14,-24(R1)
11 ADDD F16,F14,F2
12 SUBI R1,R1,#32 ;alter to 4*8
13 SD +8(R1),F16
14 BNEZ R1,LOOP
15 NOP
1 cycle stall
2 cycles stall
15 + 4 x (1+2) = 27 clock cycles, or 6.8 per iteration

## Slide 30: Unrolled Loop That Minimizes Stalls
What assumptions made when moved code?
  OK to move store past SUBI even though changes register
  OK to move loads before stores: get right data?
  When is it safe for compiler to do such changes?
1 Loop: LD F0,0(R1)
2 LD F6,-8(R1)
3 LD F10,-16(R1)
4 LD F14,-24(R1)
5 ADDD F4,F0,F2
6 ADDD F8,F6,F2
7 ADDD F12,F10,F2
8 ADDD F16,F14,F2
9 SD 0(R1),F4
10 SD -8(R1),F8
11 SUBI R1,R1,#32
12 SD +16(R1),F12
13 BNEZ R1,LOOP
14 SD 8(R1),F16 ; 8-32 = -24
14 clock cycles, or 3.5 per iteration

## Slide 31: Where are the name dependencies?
1 Loop:L.D F0,0(R1)
2 ADD.D F4,F0,F2
3 S.D 0(R1),F4 ;drop DSUBUI & BNEZ
4 L.D F0,-8(R1)
5 ADD.D F4,F0,F2
6 S.D -8(R1),F4 ;drop DSUBUI & BNEZ
7 L.D F0,-16(R1)
8 ADD.D F4,F0,F2
9 S.D -16(R1),F4 ;drop DSUBUI & BNEZ
10 L.D F0,-24(R1)
11 ADD.D F4,F0,F2
12 S.D -24(R1),F4
13 DSUBUI R1,R1,#32 ;alter to 4*8
14 BNEZ R1,LOOP
15 NOP How can remove them?

## Slide 32: Where are the name dependencies?
1 Loop: L.D F0,0(R1)
2 ADD.D F4,F0,F2
3 S.D 0(R1),F4 ;drop DSUBUI & BNEZ
4 L.D F6,-8(R1)
5 ADD.D F8,F6,F2
6 S.D -8(R1),F8 ;drop DSUBUI & BNEZ
7 L.D F10,-16(R1)
8 ADD.D F12,F10,F2
9 S.D -16(R1),F12 ;drop DSUBUI & BNEZ
10 L.D F14,-24(R1)
11 ADD.D F16,F14,F2
12 S.D -24(R1),F16
13 DSUBUI R1,R1,#32 ;alter to 4*8
14 BNEZ R1,LOOP
15 NOP
The Original “register renaming”

## Slide 33: Compiler Perspectives on Code Movement
Compiler concerned about dependencies in program
Whether or not a HW hazard depends on pipeline
Try to schedule to avoid hazards that cause performance losses
(True) Data dependencies (RAW if a hazard for HW)
  Instruction i produces a result used by instruction j, or
  Instruction j is data dependent on instruction k, and instruction k is data dependent on instruction i.
If dependent, can’t execute in parallel
Easy to determine for registers (fixed names)
Hard for memory (“memory disambiguation”) problem:
  Does 100(R4) = 20(R6)?
  From different loop iterations, does 20(R6) = 20(R6)?

## Slide 34: Unrolled Loop Detail
Do not usually know upper bound of loop
Suppose it is n, and we would like to unroll the loop to make k copies of the body
Instead of a single unrolled loop, we generate a pair of consecutive loops:
  1st executes (n mod k) times and has a body that is the original loop
  2nd is the unrolled body surrounded by an outer loop that iterates (n/k) times
  For large values of n, most of the execution time will be spent in the unrolled loop

## Slide 35: Steps Compiler Performed to Unroll
Check OK to move the S.D after DSUBUI and BNEZ, and find amount to adjust S.D offset
Determine unrolling the loop would be useful by finding that the loop iterations were independent
Rename registers to avoid name dependencies
Eliminate extra test and branch instructions and adjust the loop termination and iteration code
Determine loads and stores in unrolled loop can be interchanged by observing that the loads and stores from different iterations are independent
  requires analyzing memory addresses and finding that they do not refer to the same address.
Schedule the code, preserving any dependences needed to yield same result as the original code

## Slide 36: Not good enough due to limitations
Amount of overhead amortized with each unroll
  Overhead: 2/6 → 2/14=1/7 → 2/26=1/13
  2/iteration 2/4 iteration 2/8 iteration
Result in growth of code size
Potential shortfall in registers.
What about branch but not loop?

## Slide 37: Using Loop unrolling and scheduling with static Multiple Issue
Integer Instruction | FP instruction | Clock cycle
Loop: L.D F0, 0(R1) |  | 1
L.D F0, -8(R1) |  | 2
L.D F0, -16(R1) | ADD.D F4, F0. F2 | 3
L.D F0, -24(R1) | ADD.D F8, F6. F2 | 4
L.D F0, -32(R1) | ADD.D F12, F10. F2 | 5
S.D F4, 0(R1) | ADD.D F16, F14. F2 | 6
S.D F8, -8(R1) | ADD.D F20, F18. F2 | 7
S.D F12,-16(R1) |  | 8
DADDUI R1, R1, #-40 |  | 9
S.D F16, 16(R1) |  | 10
BNE R1, R2, Loop |  | 11
S.D F20, 8(R1) |  | 12

## Slide 38: Static Multiple issue: VLIW
VLIW: Very Long Instruction Word
Each “instruction” has explicit coding for multiple operations
  In EPIC, grouping called a “packet”
  In Transmeta, grouping called a “molecule” (with “atoms” as ops)
Tradeoff instruction space for simple decoding
  The long instruction word has room for many operations
  By definition, all the operations the compiler puts in the long instruction word are independent => execute in parallel
  E.g., 2 integer operations, 2 FP ops, 2 Memory refs, 1 branch
    16 to 24 bits per field => 7*16 or 112 bits to 7*24 or 168 bits wide
  Need compiling technique that schedules across several branches

## Slide 39: Loop Unrolling in VLIW
Memory Memory FP FP Int. op/ Clock reference 1 reference 2 operation 1 op. 2 branch
LD F0,0(R1) LD F6,-8(R1) 1
LD F10,-16(R1) LD F14,-24(R1) 2
LD F18,-32(R1) LD F22,-40(R1) ADDD F4,F0,F2 ADDD F8,F6,F2 3
LD F26,-48(R1) ADDD F12,F10,F2 ADDD F16,F14,F2 4
ADDD F20,F18,F2 ADDD F24,F22,F2 5
SD 0(R1),F4 SD -8(R1),F8 ADDD F28,F26,F2 6
SD -16(R1),F12 SD -24(R1),F16 7
SD -32(R1),F20 SD -40(R1),F24 SUBI R1,R1,#48 8
SD -0(R1),F28 BNEZ R1,LOOP 9
Unrolled 7 times to avoid delays
7 results in 9 clocks, or 1.3 clocks per iteration (1.8X)
Average: 2.5 ops per clock, 50% efficiency
Note: Need more registers in VLIW (15 vs. 6 in SS)

## Slide 40: Problems for VLIW
Technical problems
  Increase in code size
    Loop unrolling
    Unused function slots
  Limitations of lockstep operation
    A stall in any function unit may cause the entire processor to stall
Logistical problem
  Binary code compatibility
Major challenge for all multiple-issue processors
  Exploit large amounts of ILP

## Slide 41: Advanced Compiler Support for Exploiting ILP
Detecting and Enhancing Loop-level Parallelism
Eliminating Dependent Computations
Software pipelining: Symbolic loop unrolling
Global Code Scheduling
  Trace Scheduling: focus on Critical path
  Superblocks

## Slide 42: Dynamic Scheduling in P6 (Pentium Pro, II, III)
Q: How pipeline 1 to 17 byte 80x86 instructions?
P6 doesn’t pipeline 80x86 instructions
P6 decode unit translates the Intel instructions into 72-bit micro-operations (~ MIPS)
Sends micro-operations to reorder buffer & reservation stations
Many instructions translate to 1 to 4 micro-operations
Complex 80x86 instructions are executed by a conventional microprogram (8K x 72 bits) that issues long sequences of micro-operations
14 clocks in total pipeline (~ 3 state machines)

## Slide 43: Dynamic Scheduling in P6
Parameter 80x86 microops
Max. instructions issued/clock 3 6
Max. instr. complete exec./clock 5
Max. instr. commited/clock 3
Window (Instrs in reorder buffer) 40
Number of reservations stations 20
Number of rename registers 40
No. integer functional units (FUs) 2 No. floating point FUs 1 No. SIMD Fl. Pt. FUs 1 No. memory Fus 1 load + 1 store

## Slide 44: P6 Pipeline
14 clocks in total (~3 state machines)
8 stages are used for in-order instruction fetch, decode, and issue
  Takes 1 clock cycle to determine length of 80x86 instructions + 2 more to create the micro-operations (uops)
3 stages are used for out-of-order execution in one of 5 separate functional units
3 stages are used for instruction commit
Instr Fetch 16B /clk
Instr Decode 3 Instr /clk
Renaming 3 uops /clk
Execu- tion units (5)
Gradu- ation
3 uops /clk
16B
6 uops
Reserv. Station
Reorder Buffer

## Slide 45: P6 Block Diagram

## Slide 46: Pentium III Die Photo
EBL/BBL - Bus logic, Front, Back
MOB - Memory Order Buffer
Packed FPU - MMX Fl. Pt. (SSE)
IEU - Integer Execution Unit
FAU - Fl. Pt. Arithmetic Unit
MIU - Memory Interface Unit
DCU - Data Cache Unit
PMH - Page Miss Handler
DTLB - Data TLB
BAC - Branch Address Calculator
RAT - Register Alias Table
SIMD - Packed Fl. Pt.
RS - Reservation Station
BTB - Branch Target Buffer
IFU - Instruction Fetch Unit (+I$)
ID - Instruction Decode
ROB - Reorder Buffer
MS - Micro-instruction Sequencer
1st Pentium III, Katmai: 9.5 M transistors, 12.3 * 10.4 mm in 0.25-mi. with 5 layers of aluminum

## Slide 47
THANK YOU
THANK YOU